## Slide 1
CAPSTONE PROJECT | 2026
OcuSmart
AI-Powered Portable Autorefractor
Bridging Clinical Accuracy & Everyday Accessibility
Team Members
Ridhi Sood (102305055)
Prachita Garg (102305075)
Yuvraj Singh (102305087)
Aryaman Padap (102305051)
BE Third Year – Electronics Instrumentation & Control
Mentors: Dr. Gagandeep Kaur & Dr. Swati Sondhi
Thapar Institute of Engineering and Technology, Patiala

## Slide 2
Introduction
An affordable, portable AI-based autorefractor designed for objective eye screening in rural and low-resource areas. The system combines infrared illumination, optical sensing hardware, and AI-driven software to estimate refractive errors including myopia, hyperopia, astigmatism, and color blindness.
Key Innovation: Eliminates need for uncomfortable mydriatic eye drops while providing accurate refractive measurements in seconds.

## Slide 3
Need Analysis
Global Vision Crisis
Refractive errors are the most common and easily correctable causes of vision impairment worldwide.
Clinical Bottleneck
Traditional screenings require expensive, heavy equipment and trained professionals to operate.
Time-Consuming
Standard procedures need mydriatic eye drops, causing discomfort and blurry vision for hours.
Accessibility Gap
Limited access to optometric care in rural and developing regions leaves conditions undiagnosed.

## Slide 4
Objectives
01
Design Prototype
Handheld, non-mydriatic photo-screening device for affordable mass vision screening.
02
Real-Time Algorithms
Implement AI-driven detection of myopia, hyperopia, and astigmatism.
03
CVD Screening
Develop color vision deficiency testing via pupil constriction response measurement.
04
Retinal Health
Establish method for assessing overall retinal health using pupillary response.

## Slide 5
Hardware Components
Raspberry Pi 4 (4GB)
Central processing unit running Python/OpenCV vision suite and diagnostic engine.
SONY IMX296 Camera
Global shutter camera captures high-resolution retinal reflections without motion blur.
850nm IR LEDs
Safe infrared illumination captures "red reflex" without pupil constriction or discomfort.
VL53L1X ToF Sensor
Ensures correct focal distance between device and patient's eye for accurate readings.

## Slide 6
Software Architecture
Vision Suite
Python/OpenCV scripts for real-time pupil detection and red reflex geometric analysis using Hirschberg Ratio calculations.
Diagnostic Engine
AI algorithm classifies refractive errors and provides immediate "Pass/Refer" status on integrated touchscreen interface.
Chromatic Module
Software-controlled red/blue light pupillometry tests retinal sensitivity for color vision deficiency screening.

## Slide 7
Cost Analysis
Component
Category
Cost (INR)
Raspberry Pi 4
Computing
8,000
Sony IMX296 Camera
Imaging
8,000
Custom 3D Printed Housing
Hardware
500
Touchscreen Display
Interface
4,500
LED/Lens Array
Optics
2,500
Total Prototype Cost
-
23,500

## Slide 8
Design Specifications
25mm M12 Lens
Custom-aligned optical assembly for high-resolution retinal reflection capture.
850nm IR Filter
Blocks ambient light, isolates specific wavelength for clear "crescent moon" reflection analysis.
3.5-inch Touchscreen
Displays real-time automated diagnostic results with clear Pass/Refer status.
Battery-Powered
Untethered operation ensures portability for field environments and mass screening.

## Slide 9
Key Design Goals
Portability
Handheld, battery-operated unit for field use in clinics and rural environments.
Non-Invasive
No uncomfortable eye drops required—uses safe infrared illumination instead.
Speed
Results in seconds rather than minutes, enabling mass screening efficiency.
Accuracy
AI-driven computer vision provides reliable refractive error classification.
Cost-Effective
Total build cost under ₹25,000 ensures widespread accessibility.
User-Friendly
Simple interface accessible to non-expert operators in resource-limited areas.

## Slide 10
Impact & Future Vision
Revolutionizing Eye Care
OcuSmart bridges the gap between clinical accuracy and everyday accessibility, offering a solution that could transform teleophthalmology and promote equitable eye care worldwide.
Target Populations
Infants and non-verbal individuals
Rural and underserved communities
Mass screening programs
Resource-limited healthcare settings